## Slide 1: East Fork Lewis River Ridgefield Pits Restoration Design Study, Technical Oversight Group Meeting 5: Project Summary and Restoration Alternatives Discussion

## Slide 2
Technical Oversight Group Meeting 5 Objectives
Recap Prior Meetings
Summarize Physical Conditions & Stakeholder Concerns
Introduce Initial Restoration Concepts
Discuss Restoration Alternatives

## Slide 3
Technical Oversight Group Meeting Recap
Meeting 1. September 10, 2018
- Site History & Stakeholder Perspectives
fish use
channel and geomorphic conditions
flows and water temperature
mining
stakeholder concerns
ownership
restoration approach
Meeting 2. November 20, 2018
- Fish Use and Available Data
WDFW Spawning Ground Surveys (SGS)
LCEP observations, summer 2018
other

## Slide 4
Technical Oversight Group Meeting Recap
Meeting 3. April 23, 2019
- Storedahl HCP for Daybreak Mine Expansion (Tim Romanski, USFWS)
- Related Stakeholder Interests & Concerns
Meeting 4. June 27, 2019
- Geomorphic Conditions and Ridgefield Pit Fill Assessment (Inter-Fluve)
- 2018 Water Temperature Sampling Results (LCEP)
TOG meeting materials and related project documents are available for download:
http://s458607291.onlinehome.us/FTP/Ridgfield Pits_Working_Group/

## Slide 5
Key Considerations From TOG Meetings - Geomorphic
Bank erosion in Daybreak Reach (L bank US of Pit 1 & along West Daybreak Park).
Bluff erosion in Daybreak Reach (L bank immediately DS of Mill Creek).
Upstream issues potentially affecting sediment processes within Project Reach: head-cut, Daybreak bridge constriction.
Ridgefield Pits sediment trapping potentially affecting downstream processes.
Sediment deposition at tributary mouths (Mill/Manley Cr.). What is source?
Loss of anastomized system in RP reach. Decreased sinuousity in US/DS reaches.
Disconnected floodplain.
Loss of wood (forested areas and wood jams) > > decreased hydraulic roughness.
Revised estimates for Ridgefield Pits filling show considerably longer trajectories compared to WEST studies. 2075 vs. 2027.

## Slide 6
Key Considerations From TOG Meetings - Hydrologic
Summer water temperature is already warm entering project reach. Mainstem temperature does not increase appreciably through project reach.
Some of the Ridgefield Pits have higher summer temperatures than mainstem.
EFLR system possibly has become more dynamic, more flashy.
Hyporheic flows are important sources of cold water in project reach above RPs. Project actions should not degrade what refuge already exists.
Have RP avulsions impacted sub-surface flows?
Are channel geometries influencing water temperatures? Too wide and shallow?
EFLR summer flows have potentially decreased historically in project reach. Heisson data does not point to this, but water withdrawals downstream may have increased. More study needed.

## Slide 7
Key Considerations From TOG Meetings – Fish Use
Water temperature is the primary concern, followed by lack of spawning habitat.
Fall Chinook (FC), Summer steelhead (SS) and chum (C) have historically used project reach for spawning (Mason Cr. confluence upstream to Daybreak).
FC currently have the most spawning activity, but this has declined significantly. C,SS – little to no spawning currently.
C spawn in side channels. FC/SS primarily in mainstem, some side channel.
1996 avulsion into Ridgefield Pits resulted in loss of quality spawning habitat.
LCEP 2018 snorkel surveys observed several juvenile chinook using mainstem near wood cover and in warmer water. Also in cold water refuge areas.
General reach observations: decent spawning conditions, poor summer rearing, ok winter rearing.

## Slide 8
Key Considerations From TOG Meetings – Mining
Storedahl Daybreak HCP is 25-year plan. Mining is ‘supposed’ to cease in 2027.
Long-term plans for the Daybreak site are unknown.
No provisions in HCP requiring specific management or restoration measures for Ridgefield Pits. Monitoring is the only requirement.
Several stakeholders have expressed concern over enforcement of, and Storedahl’s compliance with the HCP terms, and the effectiveness of some of the conservation measures.
HCP monitoring reports have been made available online.
Potential avulsion into Daybreak is a significant concern. Has Storedahl adequately addressed this for the existing conditions? Restoration plans must not increase risk.

## Slide 9
Water Elevation and Temperature (2018)
Long term site (2012 – 2018)
- Head-cut
- Water Temp.
- Sediment inputs (unknown ?)

## Slide 10
Water Elevation and Temperature (2018)

## Slide 11
Water Elevation and Temperature (2018)

## Slide 12
Water Elevation and Temperature (2018)

## Slide 13
Water Temperature (2018)

## Slide 14
Water Temperature (2018)

## Slide 15
Water Elevation and Temperature (2018)

## Slide 16
Sediment Sampling Plan (2018)
bank cut profile
depth of refusal
surface/subsurface pebble counts

## Slide 17
Sediment Sampling – Bed Material (Surface/Armoring)

## Slide 18
Sediment Sampling – Bed Material (Surface/Armoring)

## Slide 19
Sediment Sampling – Bed Material (Surface/Armoring)
Relatively consistent size distribution throughout the study area
D10 ≈ 20mm Coarse Gravel
D50 ≈ 50mm Very Coarse Gravel
D84 ≈ 100mm Cobble

## Slide 20
Sediment Sampling – Bed Material (Subsurface)

## Slide 21
Sediment Sampling – Bed Material (Subsurface)
Two peaks in grain size, i.e. mixture of:
    Coarse components: Gravel/Cobble, ~ same as river bed
    Fine components: Sands, even silts (2mm and less)

## Slide 22
Sediment Sampling – Floodplain Material

## Slide 23
Sediment Sampling – Floodplain Material
Also has two peaks in grain size. Similar profiles to riverbed subsurface.

## Slide 24
Sediment Sampling – Vertical Bank Profile

## Slide 25
Sediment Sampling – Vertical Bank Profile

## Slide 26
Sediment Sampling – Vertical Bank Profile
Type 1: Single layer of mixed sand, gravel, cobble. Forested floodplains.
Type 2: Two layer structure with thick sand/silt layer over the Type 1 layer. More dominant.

## Slide 27
Proposed Sediment Parameters for Modeling
Sediment Type A:
bed surface layer
Sediment Type B:
bed sublayer, forested floodplain
Sediment Type C:
Bank top layer,
uniform size of
1 or 2 mm

## Slide 28
Proposed Sediment Parameters for Modeling

## Slide 29
Elevation Model: Primary Source Data
Long term site (2012 – 2018)
2010 Lower Columbia LiDAR (Corps of Engineers)

## Slide 30
Elevation Model: Primary Data Source
Long term site (2012 – 2018)
Data gaps due to standing water

## Slide 31
Elevation Model: Primary Data Source
Long term site (2012 – 2018)
Data gaps due to changes in planform over time
Channel form 2010
2010 elevation model

## Slide 32
Elevation Model: Primary Data Source
Long term site (2012 – 2018)
Channel form 2010
2017 Image
Data gaps due to changes in planform over time

## Slide 33
Bathymetric and Topographic Survey (2018)
Long term site (2012 – 2018)
Topo-bathy: 3600 points, RTK and total station
Bathy: 4 miles, single beam sonar

## Slide 34
Bathymetric and Topographic Survey (2018)
Long term site (2012 – 2018)
Topo-bathy: 3600 points, RTK and total station
Bathy: 4 miles, single beam sonar

## Slide 35
Bathymetric and Topographic Survey (2018)
Long term site (2012 – 2018)
Topo-bathy: 3600 points, RTK and total station
Bathy: 4 miles, single beam sonar

## Slide 36
Hydro/Morpho-dynamic 2D Model: surface
Long term site (2012 – 2018)

## Slide 37
Hydro/Morpho-dynamic 2D Model: model extent & drivers
Model Inputs:
Downstream water surface elevation (LCEP sensor)
Upstream flow (Heisson gage)
Optional upstream sediment supply (best estimate)
WSE
Q
SED

## Slide 38
Model hydraulic inputs: H-Q rating curve
Established relationship between upstream flow (Q) and downstream water level based on available data:
Cr, β: rating curve
constants
a: constant which
represents the
gauge reading
corresponding
to zero discharge.
Over bank flow:
In bank flow:

## Slide 39
Flood Frequency Analysis, EFLR

## Slide 40
Tuflow FV Sediment/Morpho-dynamic Model Key Features
Suspended load
  Hydraulic module  advection / dispersion
  Sedimentation / Erosion (Mehta Model)
Bedload (Meyer-Peter Mueller Model)
Morphology (adjusts bed elevation in response to sediment transport)
Multiple sediment fraction
Multiple bed layer
Armouring
2D/3D
Slide source: BWT-WBM (Tuflow FV)

## Slide 41
Tuflow FV Sediment Module: Armouring Feature
Slide source: BWT-WBM (Tuflow FV)

## Slide 42
Transport Mode Governing Equations
- Condition for sediment transport: Bed shear stress () > critical shear stress (
Look at values output by hydrodynamic (or sediment) model to get a sense of where sediment is predicted to move under different flow conditions.
Compare to known sources (imagery) to see if model is making sense
Suspended Load Erosion Model == Mehta
Mehta’s erosion model
Bedload Model == MPM
Meyer-Peter Müller’s equation

## Slide 43
Grain Size and Critical Shear Stress
Description | Grain Size (mm) | Tau,c Shields’ (1936) (N/m2) | Tau,c Soulsby’s (1997) (N/m2)
Fine Sand | 1 | 0.50 | 0.50
Gravel | 10 | 9.0 | 9.0
Coarse Gravel | 25 | 22.4 | 22.4
Cobble | 100 | 89.1 | 89.1
Slide source: BWT-WBM (Tuflow FV)

## Slide 44
Model Results: Bed Shear Stress, Q = 1000 cfs (base flow)
> for:
none
sand
gravel
cobble

## Slide 45
Model Results: Bed Shear Stress, Q = 3000 cfs (~Q1)
> for:
none
sand
gravel
cobble

## Slide 46
Model Results: Bed Shear Stress, Q = 15,000 cfs (~Q20)
> for:
none
sand
gravel
cobble

## Slide 47
Model Results: Bed Shear Stress, Q = 28,600 cfs (~Q100)
> for:
none
sand
gravel
cobble

## Slide 48
Model Results: Bed Elevation Change, post 5-yr event
-1.0
0
1.0

## Slide 49
Preliminary Model Observations
Even at base flow condition, can reach 50N/m2 in some areas, which is strong enough to move bed material smaller than “coarse gravel”.
At a 1-yr flood event, can reach 100N/m2 in limited areas. The majority of bed material ‘can’ move, but cobble forms an armouring layer in most areas. This is a high frequency event and the bank erosion may shift the stream banks over time.
Under the 5-yr flood event, water can get almost everywhere. can reach 150N/m2 even in the potential river course at the south side of the domain.
Much more to come!

## Slide 50
Preliminary Model Observations
Questions?