## Slide 1: Ridgefield Pits Meeting
Welcome
*Please mute to start*
*Send comments via chat*
*Let us know if you are having any issues*
March 7th
Meeting Organizer
Paul Kolp- Lower Columbia Estuary Partnership

## Slide 2: AGENDA
Recap. of where we are
Over the last several months- we’ve been focused on Alternative 3-Revised (Alt. 3 + Alt. 2)
Example Floodplain Grading- LCFEG (Brice C.)
Restoration Alternatives- Technical Analysis (presentation & discussion)
Next steps

## Slide 3: Analysis (since last meeting)- Alt 3 Revised
Creating habitat for fish: sediment, temperature, depths, velocities
Eliminate warm water sinks & connect to known cooler water
Floodplain inundation
Sediment transport through site & downstream (replenish gravels)
Grading plan
Risks to infrastructure

## Slide 4: Example Project
…..South Fork Toutle River Tributary…….

## Slide 5
Pits Alternatives- Cut/Fill Balance
Existing Grade
Alt 3. multi-thread, 1st iteration
External Fill required: ~400,000 cy
External Fill required: -72,000 cy
External Fill required: 44,000 cy
Floodplain x-section profiles
Channel longitudinal profiles
Alt 3 Revised.- multi-thread, 2nd iteration
Alt 3 Revised.- multi-thread, 3rd iteration

## Slide 6
Grading Plan

## Slide 7
Existing Condition
Alternative 3
Alternative 3 - hybrid
Baseflow Inundation – 35 cfs
Existing Condition: channel confined within deep pits
Alt 3 and Hybrid:
  surface area available for solar heat addition is reduced
  Hybrid retains accessible alcoves at low flows
Variation in depth will increase as designs are refined at the channel unit scale (pools, tailouts, riffles).

## Slide 8
Existing Condition
Alternative 3
Alternative 3 - hybrid
Typical winter flow – 1,000 cfs
Existing Condition: channel confined within deep pits
Alt 3 and Hybrid:
  deep water habitat is reduced significantly
  flow mostly contained within channels with some shallow wetlands

## Slide 9
Existing Condition
Alternative 3
Alternative 3 - hybrid
Moderate winter flow – 3,000 cfs
Existing Conditions: channel confined within deep pits
Alt 3 and Hybrid: Shallow floodplain inundation throughout much of reach

## Slide 10
Existing Condition
Alternative 3
Alternative 3 - hybrid
Annual Flood – 5,000 cfs
Existing Conditions: channel confined within deep pits
Alt 3 and Hybrid: Floodplain inundation covers most of pits reach

## Slide 11
Existing Condition
Alternative 3
Alternative 3 - hybrid
100 year flood – 28,600 cfs
Existing Conditions: High ground not inundated within pits
Alt 3 and Hybrid: Increase in floodplain inundation
Hybrid has increased depth across the floodplain at downstream end of the project
Variation in depth across the floodplain will increase as grading is refined to add form roughness and support a variety of riparian vegetation communities

## Slide 12
Existing Condition
Alternative 3
Alternative 3 - hybrid
~Q1 - 5000 cfs
Existing Conditions: Sharp transition from gravels to fines in pits
Alt 3 and Hybrid:
  Reduction in fines
  Restored gravel transport throughout
  Coarse gravel transport still limited at this flow

## Slide 13
Existing Condition
Alternative 3
Alternative 3 - hybrid
Q100 – 28,600 cfs
Existing Conditions: Pits segment still limited in transport capacity of coarse material - Discontinuity
Alt 3 and Hybrid: Restored coarse gravel transport and continuity to downstream reach
Infrastructure considerations
  BPA power line towers
  Daybreak Pits interface
  Bluffs

## Slide 14
Temperature Analysis: Simulated Water Temperature @ 35 cfs
Model temperature input sources: - Quantum Thermal IR survey (2020)
- LCEP temp. monitoring (2018)
Model results observations for restoration alternatives:
- Warm water pits #5 and #7 eliminated
- Potential to provide connectivity to colder side channel waters
- Potential to provide connectivity to colder Pits #8 and 2
Pit 8 and side channel disconnected from river
Additional thermal benefits predicted for restoration alternatives:
Reduced channel surface area should reduce heating potential
Existing Grade Alternative 3 Hybrid 3-chan Alternative
Wetted surface area (acres) 20.7 19.6 14.6
Existing Conditions
Alternative 3
Alternative 3- Revised

## Slide 15
Expected Geomorphic Trajectory
Existing Conditions:
Continued confinement within pits for >70 years
Very slow delta growth
Extremely depositional – dominated by fines downstream of delta
Limited floodplain inundation
Limited access to potential channel migration zone
Proposed Conditions:
Increased floodplain inundation
Increased channel migration zone width
Gravel transport (and deposition) restored throughout
Still DEPOSITIONAL! – but less than existing. Channels will be expected to continue to evolve due to channel response to bedload aggradation
Full pits area (channels and floodplain) will aggrade more uniformly over time, as opposed to the pronounced delta that currently exists

## Slide 16
Risk Considerations
Existing Conditions:
High risk to habitat (channel form, temperature, food, invasives, fines)
Low risk to infrastructure (due to continued confinement)
Proposed Conditions:
Habitat improvement (immediate habitat created and trajectory set for increased habitat over time)
Risk of Daybreak Pits avulsion/breaching? – Possible due to increased channel migration zone and uncertainty with future planform changes. Will likely need to be addressed via armoring.
Risk to BPA Powerline Towers? – Possibly little-to-no risk based on no significant changes to floodplain inundation across powerline alignment. Warrants further investigation as part of Final Design plus consultation with BPA.
Risk to bluff erosion upstream? – Likely not based on model results and area of expected channel changes.

## Slide 17: Next Steps
Present the results of model runs
Model revised alternatives (as needed)- Al3 Revised (this meeting)
Present results to the group- today
Preferred alternatives
Develop preliminary designs at three locations, engineering plans
cost estimates, quantities.

## Slide 18: We did not get to the next 3 slides in the Meeting

## Slide 19
Existing Conditions
Mill-Manley Confluence
Alternative 5
  Objective – increase scour of Mill confluence gravels in cold water alcove
  Grading at the upstream edge of the gravel bar to encourage high flows routed through confluence zone
Alternative 5

## Slide 20
Existing Conditions
Alternative 5
Mill-Manley Confluence: ~Q1 - 5000 cfs
Alt 5 – Sediment Transport
  Slight increase in shear stress in Alt 5
  No dramatic changes to the sediment transport capacity at the confluence

## Slide 21
Mill-Manley Confluence
Geomorphic Trajectory and Risk
  Channel migrating to the north over the last 30 years
  Continued migration will lengthen back-bar channel fed by Mill and Manley
  Creating a scour channel has uncertain outcome especially given continued channel migration
  Existing house on top of bluff currently being undermined
  Effects on bluff erosion uncertain as channel migrates

## Slide 22: END

## Slide 23: Restoration Alt.’s- Voting From Last Year Meeting
Alt. 1- No action/passive recovery
Alt. 2- Relocate main channel back to pre-1996 avulsion
Alt. 2a- Relocate river into a portion of its pre-avulsion flow path
Alt. 3- Full Floodplain & Pits Re-Grade
Alt. 3a- Select Floodplain & Pits Regrade
Notes: Restoration Alternatives Prioritized- Alt 3 (multi-thread channel)
- TOG to comment on refinement March 30
Channel migration zone
Allowing riverine processes
Cold water